## Slide 1: CHAPTER-5 DESIGN OF SHAFTS
Tribhuwan University
Institute of Engineering
Pulchowk Campus

## Slide 2: DESIGN OF SHAFT BASED ON Minimum shear stress theory
Q.1. The layout of an intermediate shaft of a gear box supporting two spur gears B and C is shown in figure below. The shaft is mounted on two bearings A and D. The pitch circle diameters of gears B and C are 900 and 600 mm respectively. The material of the shaft is steel FeE 580 (Sut = 770 N/mm2 and Syt = 580 N/mm2). The factors kb and kt of ASME code are 1.5 and 2.0 respectively. Determine the shaft diameter using the ASME code.
Assume that the gears are connected to the shaft by means of keys.

## Slide 3: DESIGN OF SHAFT BASED ON Minimum shear stress theory

## Slide 4: Steps involved
Permissible (or Allowable) Shear Stress.
Load (Vertical and Horizontal), Bending Moment (Vertical and horizontal) and Torsional Diagram.
Resultant Bending Moment from the Horizontal and Vertical Moment Diagram.
Shaft diameter using ASME Code.

## Slide 5: Permissible (or allowable) shear stress
Permissible shear stress
= 0.30 Syt
or, = 0.18 Sut
When keyways are present on the shaft,
= 0.75 (minimum value obtained from above criteria)
Choose whichever has minimum value

## Slide 6: Load Diagram (vertical and horizontal plane)
A
B
C
D
1609 N
6631.5 N
Ay
Dy
900 mm
900 mm
900 mm
Az
Dz
A
B
C
D
4421 N
2413.67 N
900 mm
900 mm
900 mm
Ay = -1137.83 N
Dy = -3884.67 N
Az = -2142.78 N
Dz = 135.45 N
x
y
x
z
Guiding Equations
Ay + Dy + 6631.5 -1609 = 0
-1609 (900) + 6631.5 (1800) + Dy (2700) = 0
Guiding Equations
Az + 4421 – 2413.67 + Dz = 0
-4421 (900) + 2413.67 (1800) – Dz (2700) = 0
Vertical Plane (Load Diagram)
Horizontal Plane (Load Diagram)

## Slide 7: Load, B.M. and Torsional Diagram (vertical and horizontal plane)
2142.78 N
135.45 N
A
B
C
D
4421 N
2413.67 N
900 mm
900 mm
900 mm
A
B
C
D
1609 N
6631.5 N
1137.83 N
3884.67 N
900 mm
900 mm
900 mm
x
y
x
z
Vertical Plane (Load Diagram)
Horizontal Plane (Load Diagram)
Bending Moment Equation
Mv(x) = -1137.83 x - |1609 (x-900)| + |6631.5 (x-1800)|
Bending Moment Equation
Mh(x) = 2142.78 x – |4421 (x-900)| + |2413.67 (x-1800)|

## Slide 8: Load, B.M. and Torsional Diagram (vertical and horizontal plane)
Bending Moment is maximum at C, i.e. Mc (Resultant) = 3498318.327 N.mm
x
y
x
z
A
B
C
D
1024047
3496194
121896
A
B
C
D
1928502
Vertical Plane (BM Diagram)
Horizontal Plane (BM Diagram)
Mv(x) = -1137.83 x - |1609 (x-900)| + |6631.5 (x-1800)|
Mh(x) = 2142.78 x – |4421 (x-900)| + |2413.67 (x-1800)|

## Slide 9: Load, B.M. and Torsional Diagram (vertical and horizontal plane)
Torsional Moment Diagram
TB = TC = 1989450 N.mm
A
B
C
D
1989450

## Slide 10: MSS THEORY DESIGN EQUATIONS
Compute d from above equation.

## Slide 11: WHAT DOES MSS THEORY SAYS ???
The failure of a mechanical component subjected to bi-axial or tri-axial stresses occurs when the maximum shear stresses at any point in the component becomes equal to the maximum shear stress in the standard specimen of the tension test, when yielding starts.
The maximum shear stress theory predicts that the yield strength in shear (Ssy) is half of the yield strength in tension (Syt), i.e.,
Ssy = 0.5 Syt

## Slide 12: DESIGN OF SHAFT based on fatigue failure analysis
Q.2. The rotating solid steel shaft is simply supported by bearings at points B and C and is driven by a gear (not shown) which meshes with the spur gear at D, which has a 150-mm pitch diameter. The force F from the drive gear acts at a pressure angle of 20. The shaft transmits a torque to point A of TA = 340 N.m. The shaft is machined from steel with Syt= 420 MPa and Sut = 560 MPa. Using a factor of safety of 2.5, determine the minimum allowable diameter of the 250-mm section of the shaft based on fatigue failure analysis.
Assume sharp fillet radii at the bearing shoulders for estimating stress-concentration factors.

## Slide 13: DESIGN OF SHAFT based on fatigue failure analysis
Shigley’s Book Problems 7-3

## Slide 14: STEPS INVOLVED
Load Diagram (VP and HP), BM Diagram (VP and HP) and Torsional Diagram
Alternating and Mid-range components of Moment and Torsion
Fatigue stress – concentration factors (kf and kfs)
Von-Mises Stresses ()
Endurance Limit
Failure Criterion Selection (Mod Goodman, Gerber, ASME-Elliptic, or Soderberg)
Assumptions refinement
Iteration with refined assumptions (or Estimates)

## Slide 15: Load Diagram (VP and HP)
x
y
A
B
C
D
By
Cy
250 mm
100 mm
1650 N
A
B
C
D
Bz
Cz
250 mm
100 mm
4533.34 N
x
z
By = -660 N
Cy = 2310 N
Bz = 1813.33 N
Cz = -6346.67 N
Vertical Plane (Load Diagram)
Horizontal Plane (Load Diagram)
Guiding Equations
By + Cy – 1650 = 0
Cy (250)-1650 (350) = 0
Guiding Equations
Bz + Cz + 4533.34 = 0
-Cz (250) – 4533.34 (350) = 0

## Slide 16: Load Diagram (VP and HP)
x
y
A
B
C
D
2310 N
250 mm
100 mm
1650 N
660 N
x
z
A
B
C
D
1813.33 N
6346.67 N
250 mm
100 mm
4533.34 N
Vertical Plane (Load Diagram)
Horizontal Plane (Load Diagram)
Bending Moment Equation
Mv(x) = -660 x + |2310 (x-250)|
Bending Moment Equation
MH(x) = -1813.33 x + |6346.67 (x-250)|

## Slide 17: BM Diagram (VP and HP)
Bending Moment is maximum at C, i.e. Mc (Resultant) = 482426.529 N.mm = 482.43 N.m
x
y
x
z
A
B
C
D
165000
A
B
C
D
453332.5
Vertical Plane (BM Diagram)
Horizontal Plane (BM Diagram)
Mv(x) = -660 x + |2310 (x-250)|
MH(x) = -1813.33 x + |6346.67 (x-250)|

## Slide 18: Load, B.M. and Torsional Diagram (vertical and horizontal plane)
Torsional Moment Diagram
TA = TC = 340000 N.mm = 340 N.m
A
B
C
D
340000 N.mm

## Slide 19: Alternating and MIDRANGE components
Since the shaft is rotating with constant bending moment, the bending stress is completely reversed.
Ma = 482.43 N.m & Mm = 0
Also the torsion is steady.
Ta = 0 & Tm = 340 N.m

## Slide 20: Fatigue stress concentration (kf and kfs)
Kf = 1 + q (Kt – 1) & Kfs = 1 + qs (Kts – 1)
For sharp fillet radius, refer Table 7-1
Kt = 2.7 and Kts = 2.2
For notch-sensitivity factor
Since fillet radius is not given;
Initially, let us assume
q = 0.8 and qs = 0.9
Note:
You can assume any value of q and qs.
(Later these can be checked once fillet radius is determined)
Kf = 2.4 & Kfs = 2.1

## Slide 21: Von-mises stress ()
From above equations, we have
=
=

## Slide 22: Determining Endurance limit (Se)
For endurance limit, we have
Here,
Se’ = 0.5 (560) = 280 MPa

## Slide 23: Endurance limit (Se)
Surface factor,
For ‘a’ and ‘b’, refer to Table 6-2
a = 4.51 and b = - 0.265

## Slide 24: Endurance limit (Se)
Size factor,
Since, diameter is unknown
So, let us assume initially
kb = 0.85
(Later it can be checked once diameter is computed)

## Slide 25: Endurance limit (Se)
Other Factors
Load modification factor, kc = 1
Temperature modification factor, kd = 1
Reliability factor, ke =1
Miscellaneous effects modification factor, kf =1
Note: Use values of 1 unless otherwise an information is given

## Slide 26: Endurance limit (Se)
Computing Endurance Limit
Endurance Limit, Se = (0.84)(0.85)(1)(1)(1)(1)(280) = 199.92 = 200 MPa (approx.)

## Slide 27: Failure Criteria selection
DE – Soderberg
DE - Goodman
DE – Gerber
DE- ASME Elliptic

## Slide 28: Failure Criteria selection (DE-soderberg)
According to DE-Soderberg
Replace & with & respectively.
Substituting values in above equations we get,
On Solving
d = 0.057 m = 57 mm

## Slide 29: Failure Criteria selection (DE-goodman)
According to DE-Goodman
Replace & with & respectively.
Substituting values in above equations we get,
On solving
d = 0.056 m = 56 mm

## Slide 30: Failure Criteria selection (DE-gerber)
According to DE-Gerber
Replace & with & respectively.
Substituting values in above equations we get,
On solving
d = 0.0534 m = 53.4 mm

## Slide 31: Failure Criteria selection (DE-asme elliptic)
According to DE-ASME elliptic
Replace & with & respectively.
Substituting values in above equations we get,
On solving
d = 0.05338 m = 53.38 mm

## Slide 32: Refinement of assumptions
With any diameter computed above, we have to now refine our assumptions made earlier.
Let us assume d = 53.4 obtained from DE-ASME Elliptic. You can choose any obtained value of diameter.
Surface factor, (no change)
Size factor, kb = 0.81

## Slide 33: Refinement of earlier assumptions
Assuming Sharp fillet radius, from Table 7-1
r/d = 0.02
r = 1.07 mm
Kt = 2.7
Kts = 2.2

## Slide 34: Refinement of earlier assumptions
For notch-sensitivity factor, referring to Figure 6-20 and 6-21
q = 0.7 & qs = 0.75
0.7
0.75

## Slide 35: Refinement of earlier assumptions
For fatigue stress-concentration factor
Kf = 1 + q (Kt – 1) & Kfs = 1 + qs (Kts – 1)
Kf = 1 + 0.7 (2.7 - 1) & Kfs = 1 + 0.75 (2.2 – 1)
So,
Kf = 2.19 & Kfs = 1.9

## Slide 36: ITERATIONS WITH REFINED assumptions
Refined Endurance Limit, Se = (0.84)(0.81)(1)(1)(1)(1)(280) = 190.51 MPa = 191 MPa (approx.)
Now,
Iterate the whole process of the particular failure criteria using the refined assumptions until you get the constant value of ‘d’.
After iterations, finally
d = 53 mm

## Slide 37: General steps in solving fatigue failure problems
Generate two stress elements – alternating stresses and midrange stresses
Apply appropriate fatigue stress-concentration factors to each of the stresses; i.e., apply kf for the bending stresses, kfs for the torsional stresses.
Calculate von Mises stress for each of these two stress elements, and .
Select a fatigue failure criterion (modified Goodman, Gerber, ASME-Elliptic, or Soderberg) to complete the fatigue analysis.
For endurance limit, Se, use the endurance limit modifiers, ka, kb and kc for bending.

## Slide 38: Determining fatigue factor of safety
Q.3. The shaft shown in the figure is driven by a gear at the right keyway, drives a fan at the left keyway, and is supported by two deep-groove ball bearings. The shaft is made from AISI 1020 cold-drawn steel. At steady-state speed, the gear transmits a radial load of 1.1 kN and a tangential load of 3 kN at a pitch diameter of 200 mm.
Determine fatigue factors of safety at any potentially critical locations.

## Slide 39: DEEP GROOVE BALL BEARINGS
Deep groove ball bearing-Single Row

## Slide 40: STEPS INVOLVED
Ultimate Tensile Strength (Sut) and Yeild Tensile Strength (Syt)
Possible critical locations
Load Diagram, BM Diagram and Torsional Diagram
Fatigue Factor of Safety at possible critical locations

## Slide 41: Ultimate Tensile Strength (Sut) and Yield Tensile Strength (Syt)
Shaft Material- AISI 1020 Cold Drawn Steel
- Refer to Table A-20 from Shigley’s Book, Page 1040
- Refer to Table 1-1 from Machine Component Design Data Handbook, Page 1
Ultimate Tensile Strength (Sut) = 470 Mpa
Yield Tensile Strength (Syt) = 390 MPa

## Slide 42: Ultimate Tensile Strength (Sut) and Yield Tensile Strength (Syt) Referring table
Sut = 470 MPa
Syt = 390 MPa

## Slide 43: Possible critical locations
A
B
C
D
E
F
O
A & C = Approximate effective center of Fan and Gear respectively
B & F = Approximate effective center of Bearings
D = Groove
E = Shoulder
O = Reference Point
OA = 25 mm
OB = 60 mm
OC = 229 mm
OD = 250.5 mm
OE = 265 mm
OF = 310 mm

## Slide 44: Load Diagram, BM DIAGRAM & TORQUE DIAGRAM Load Diagram
x
y
O
A
C
F
By
1100 N
B
D
E
Fy
x
z
Vertical Plane (Load Diagram)
Horizontal Plane (Load Diagram)
O
A
C
F
Bz
B
D
E
3000 N
Fz
Guiding Equations
By + 1100 + Fy = 0
1100 (BC) + Fy (BF) = 0
By = -356.4 N
Fy = -743.6 N
Bz = -972 N
Fz = -2028 N
Guiding Equations
Bz + Fz + 3000 = 0
-3000 (BC) – Fz (BF) = 0

## Slide 45: Load Diagram, BM DIAGRAM & TORQUE DIAGRAM Load Diagram (CONTD…)
x
y
O
A
C
F
972 N
3000 N
B
D
E
2028 N
x
z
Vertical Plane (Load Diagram)
Horizontal Plane (Load Diagram)
O
A
C
F
356.4 N
B
D
E
1100 N
743.6 N
Bending Moment Equation (Taking B as reference)
Mv(x) = -356.4 x + |1100 (x-BC)|
Bending Moment Equation (Taking B as reference)
MH(x) = 972 x - |3000 (x-BC)|

## Slide 46: Load Diagram, BM DIAGRAM & TORQUE DIAGRAM BM Diagram
x
y
x
z
Vertical Plane (BM Diagram)
Horizontal Plane (BM Diagram)
Bending Moment Equation (Taking B as reference)
Mv(x) = -356.4 x + |1100 (x-BC)|
Mv (O) = Mv(A) = Mv(B) = 0 ;
Mv(C) = -60231.6 N.mm ; Mv(D) = -44244.2 N.mm;
Mv(E) = -33462 N.mm ; Mv(F) = 0
Bending Moment Equation (Taking B as reference)
MH(x) = 972 x - |3000 (x-BC)|
MH (O) = MH(A) = MH(B) = 0 ;
MH(C) = 164268 N.mm ; MH(D) = 120666 N.mm;
MH(E) = 91260 N.mm ; MH(F) = 0
O
A
C
F
B
D
E
O
A
C
F
B
D
E

## Slide 47: Load Diagram, BM DIAGRAM & TORQUE DIAGRAM TORQUE DIAGRAM
Torsional Moment Diagram
TO = TD = TE = 0 N.mm
TA = TB = TC = 3000 (100) = 300,000 N.mm
O
A
C
F
B
D
E

## Slide 48: Load Diagram, BM DIAGRAM & TORQUE DIAGRAM RESULTANT BM DIAGRAM & TORQUE DIAGRAM
MR (O) = MR(A) = MR(B) = 0 ;
MR(C) = 174962.343 N.mm ; MR(D) = 128521.721 N.mm;
MR(E) = 97201.302 N.mm ; MR(F) = 0
Resultant BM Diagram
Torque Diagram
O
A
C
F
B
D
E
174,962.343
128,521.721
97,201.302
TO = TD = TE = 0 N.mm
TA = TB = TC = 3000 (100) = 300,000 N.mm
O
A
C
F
B
D
E
300,000

## Slide 49: Fatigue Factor of safety at critical position
A
B
C
D
E
F
O
Determining factor of safety using DE-GERBER Fatigue Failure Criteria except at location A

## Slide 50: Critical location A (Keyway)
MR(A) = 0
T(A) = 300,000 N.mm
Location A has only a steady high torque value, so from MSS Theory
Where,
T = T(A) = 300,000 N.mm,
r = radius of shaft at A = 12.5 mm
J = polar moment of inertia = = = 38349.52
Sy = Syt = 390 MPa
Rearranging and Solving equation (5-3), we get
Fatigue factor of safety, nf = = = 1.994

## Slide 51: Critical location C (Keyway)
MR(C) = 174962.343 N.mm
T (C) = 300,000 N.mm
Stress concentration factors
For r/d ratio, refer to Table 7-1 (Page 373)
Kt = 2.14
Kts = 3.0
r/d = 0.02
We have, d = 44. So, r = 0.02 (44) = 0.88

## Slide 52: Critical location C (Keyway) (CONTD…)
For notch-sensitivity factor, referring to Figure 6-20 and 6-21
q = 0.65
qs = 0.70
0.65
0.70

## Slide 53: Critical location C (Keyway) (CONTD…)
Fatigue stress concentration factor, Kf and Kfs
Kf = 1 + q (Kt – 1) = 1 + 0.65 (2.14 - 1) = 1.741
&
Kfs = 1 + qs (Kts – 1) = 1 + 0.7 (3.0 - 1) = 2.4

## Slide 54: Critical location C (Keyway) (CONTD…)
Endurance Limit (Se)
Where,
= 0.5 = 235 MPa

## Slide 55: Critical location C (Keyway) (CONTD…)
Surface Factor (Ka)
For ‘a’ and ‘b’, refer to Table 6-2
a = 4.51 and b = - 0.265
83

## Slide 56: Critical location C (Keyway) (CONTD…)
Size Factor (Kb)
Since d = 44 mm
Kb =

## Slide 57: Critical location C (Keyway) (CONTD…)
Other modifying factors
Load modification factor, kc = 1
Temperature modification factor, kd = 1
Reliability factor, ke =1
Miscellaneous effects modification factor, kf =1

## Slide 58: Critical location C (Keyway) (CONTD…)
Computing Endurance Limit
Endurance Limit, Se = (0.883)(0.827)(1)(1)(1)(1)(235) = 171.607 = 171.6 MPa (approx.)

## Slide 59: Critical location C (Keyway) (CONTD…)
Midrange and Alternating Components (Von Misses Stresses)
Torsion is steady and the constant bending moment produces completely reversed stresses,
So, Mm = Ta = 0
& Ma (C) = 174962.343 N.mm and Tm (C) = 300,000 N.mm
From above equations, we have
= 36.424 MPa
= 74.560 MPa

## Slide 60: Critical location C (Keyway) (CONTD…)
DE- GERBER FAILURE CRITERIA
Replace & with & respectively.
Substituting values in above equations we get,
On solving
nf = 3.48

## Slide 61: Critical location D (Groove)
MR(D) = 128521.721 N.mm
T (D) = 0 N.mm
Stress concentration factors, Kt and Kts
For round bottom groove, refer to Figure A-15-14
r/d = 2.5/(44 - 5) = 0.064
D/d = 44/(44 - 5) = 1.128
2.05
From Figure A-15-14
Kt = 2.05
What about the value of Kts ???
Kts is used for computing Kfs. Kfs is used for multiplying the value of Torque. But T(D) = 0. So, no need to compute Kts

## Slide 62: Critical location D (Groove) (CONTD…)
For notch-sensitivity factor, referring to Figure 6-20 and 6-21
q = 0.78
0.78
What about qs ???

## Slide 63: Critical location D (Groove) (CONTD…)
Fatigue stress concentration factor, Kf and Kfs
Kf = 1 + q (Kt – 1) = 1 + 0.78 (2.05 - 1) = 1.82
&
Kfs = 1 + qs (Kts – 1) = … ???

## Slide 64: Critical location D (Groove) (CONTD…)
Endurance Limit (Se)
Where,
= 0.5 = 235 MPa

## Slide 65: Critical location D (Groove) (CONTD…)
Surface Factor (Ka)
For ‘a’ and ‘b’, refer to Table 6-2
a = 4.51 and b = - 0.265
83

## Slide 66: Critical location D (Groove) (CONTD…)
Size Factor (Kb)
Since d = 39 mm
Kb = 8

## Slide 67: Critical location D (Groove) (CONTD…)
Other modifying factors
Load modification factor, kc = 1
Temperature modification factor, kd = 1
Reliability factor, ke =1
Miscellaneous effects modification factor, kf =1

## Slide 68: Critical location D (Groove) (CONTD…)
Computing Endurance Limit
Endurance Limit, Se = (0.883)(0.838)(1)(1)(1)(1)(235) = 173.889 = 174 MPa (approx.)

## Slide 69: Critical location D (Groove) (CONTD…)
Midrange and Alternating Components (Von Misses Stresses)
Torsion is steady and the constant bending moment produces completely reversed stresses,
So, Mm = Ta = 0
& Ma (D) = 128521.721 N.mm and Tm (D) = 0 N.mm
From above equations, we have
= 40.166 MPa
= 0 MPa

## Slide 70: Critical location D (Groove) (CONTD…)
DE- GERBER FAILURE CRITERIA
Replace & with & respectively.
Substituting values in above equations we get,
On solving
nf = 4.332

## Slide 71: Critical location E (Shoulder)
MR(E) = 128521.721 N.mm
T (E) = 0 N.mm
Stress concentration factors, Kt and Kts
For round bottom groove, refer to Figure A-15-9
r/d = 3/35 = 0.086
D/d = 50/35 = 1.43
1.7
From Figure A-15-9
Kt = 1.7
What about the value of Kts ???
Kts is used for computing Kfs. Kfs is used for multiplying the value of Torque. But T(E) = 0. So, no need to compute Kts

## Slide 72: Critical location E (Shoulder) (CONTD…)
For notch-sensitivity factor, referring to Figure 6-20 and 6-21
q = 0.79
0.79
What about qs ???

## Slide 73: Critical location E (Shoulder) (CONTD…)
Fatigue stress concentration factor, Kf and Kfs
Kf = 1 + q (Kt – 1) = 1 + 0.79 (1.7 - 1) = 1.553
&
Kfs = 1 + qs (Kts – 1) = … ???

## Slide 74: Critical location E (Shoulder) (CONTD…)
Endurance Limit (Se)
Where,
= 0.5 = 235 MPa

## Slide 75: Critical location E (Shoulder) (CONTD…)
Surface Factor (Ka)
For ‘a’ and ‘b’, refer to Table 6-2
a = 4.51 and b = - 0.265
83

## Slide 76: Critical location E (Shoulder) (CONTD…)
Size Factor (Kb)
Since d = 35 mm
Kb = 8

## Slide 77: Critical location E (Shoulder) (CONTD…)
Other modifying factors
Load modification factor, kc = 1
Temperature modification factor, kd = 1
Reliability factor, ke =1
Miscellaneous effects modification factor, kf =1

## Slide 78: Critical location E (Shoulder) (CONTD…)
Computing Endurance Limit
Endurance Limit, Se = (0.883)(0.848)(1)(1)(1)(1)(235) = 175.964 = 176 MPa (approx.)

## Slide 79: Critical location E (Shoulder) (CONTD…)
Midrange and Alternating Components (Von Misses Stresses)
Torsion is steady and the constant bending moment produces completely reversed stresses,
So, Mm = Ta = 0
& Ma (E) = 97201.302 N.mm and Tm (E) = 0 N.mm
From above equations, we have
= 35.862 MPa
= 0 MPa

## Slide 80: Critical location E (Shoulder) (CONTD…)
DE- GERBER FAILURE CRITERIA
Replace & with & respectively.
Substituting values in above equations we get,
On solving
nf = 4.908

## Slide 81: !!! THANK YOU !!!